## Slide 1: Aerodynamic Design of a Fowler Flap for a Hybrid Laminar Flow Control Airfoil
Holenarsipura, Shrinidhi, 06/05/2025
Advisor,
Dr.-Ing Stanislav Karpuk
Notes: Good Afternoon Everyone, Thank you for joining for the presentation of my Studienarbeit titled “Aerodynamic Design of a Fowler Flap for a Hybrid Laminar Flow Control Airfoil”, under the guidance of Dr. Karpuk. I hope you can take away something new this afternoon.

## Slide 2: Contents
  Tasks
  Objective
  Introduction
  Methodology
  Trade studies
  Results
  Summary
  Future work
Notes: In today's presentation I will take you through the tasks undertaken, objective of the research followed by the Introduction, Methodology, Trade studies performed, Results obtained, Summary and Future work at the last

## Slide 3: Contents
  Tasks
  Objective
  Introduction
  Methodology
  Trade studies
  Results
  Summary
  Future work
Notes: Starting with the Tasks and Objective

## Slide 4: Tasks
Define and modify an existing design methodology for a rapid CFD analysis of airfoils.
Perform parametric studies of a Fowler flap.
Obtain a new design and compare key aerodynamic characteristics between the original and the final configurations.
Objective
Maximize lift for takeoff (15°) and landing (30°) flap settings.
Notes: The main tasks for this Studienarbeit was to define and modify the existing methodology
Followed by performing parametric studies of the Fowler Flap
And obtaining a new design and comparing key aerodynamic characteristics between the baseline and the final configuration
The objective was to maximize the lift for at 15° and 30° flap deflections, corresponding to the take off and landing configurations.

## Slide 5: Contents
  Tasks
  Objective
  Introduction
  Methodology
  Trade studies
  Results
  Summary
  Future work
Notes: Starting with the Introduction

## Slide 6: High-lift devices
Fig 2: Mechanism of the Fowler flap
[1], [2].
Fig 1: Effect of high-lift devices
on the lift coefficient (CL) and the angle of attack (α) [1].
Notes: The formula in the middle represents how Lift is defined
Lift can be increased by
Either increasing the density of air – impossible at landing and take off conditions
Change in velocity – not possible at landing condition because we need to land at reduced velocity for safer landing
Change in reference area – Yes, with devices such as the Fowler flaps with the mechanism on the right, where they extend outward and downward – But, not by much
Change in the Lift Coefficient – Yes, by making the design more aerodynamic, increasing the overall lift and reduce drag – Substantial increase in Lift
The question is Why are high lift devices such as Fowler Flaps necessary?
The answer is, they offer higher Lift coefficients at the same angle of attacks and also delay flow separation
But, how is it beneficial?
The fig on the right represents how a fowler flap works, it extends outwards and downwards – effectively increasing the camber, and also the reference area The flap deflection creates pressure distribution – crucial for lift generation followed by Increased Circulation and the Slot Effect – reenergizing the boundary layer and delaying flow separation.

## Slide 7: Contents
  Tasks
  Objective
  Introduction
  Methodology
  Trade studies
  Results
  Summary
  Future work

## Slide 8: PyAeroSweep framework
Fig 6: PyAeroSweep
Framework.
Python
Fidelity Pointwise
SU2CODE
Notes: One of the most integral part of this research is The PyAeroSweep is a Python based framework that automates Pre-Processing Meshing CFD analysis
Processes – Developed by Dr. Karpuk, here at the IFL. It uses Fidelity pointwise as the CFD meshing tool with commands written into the native Glyph scripts with mesh configurations
And SU2 - an Opensource CFD solver coupled with RANS simulations.
The Input Data module contains all the user defined inputs such as the mesh settings, free stream conditions and convergence criterias This is then (Explain the flow chart)…..

## Slide 9: Geometry definition
Fig 3: Key flap geometry definitions [3].
Fig 4: (a) Horizontal overlap x_gap and (b) Vertical gap y_gap definition.
Notes: The 3 key geometric curves used in geometric definition are:
Circular Arc
Conical Curve
Spline Curve
As represented in Figure 3 in green, blue and red colors.
This has been adopted from previous research.
But, 2 distinct parameters
X GAP
Y GAP
Are added to the geometric parameters, wherein these two parameters play a major role wrt flap aerodynamics.

## Slide 10: Geometric parameters – baseline flap
Fig 5: PARSEC airfoil.
Table 1: Geometric parameters for the baseline flap design.
15° droop nose
15°/30° flap deflection
Notes: Figure 5 represents the PARSEC airfoil including the flap – deflected at 15 ° and the nose drooped at a fixed angle of 15°.
The table to the right represents the parameters of the Flap, defined wrt
Airfoil and
Flap
With the baseline values for each.

## Slide 11: Mesh generation – Fidelity Pointwise
Fig 7: Computational mesh around the HLFC airfoil.
Fig 8: Detailed view of the computational mesh around the Fowler flap.
Notes: The computational mesh is generated with Poitnwise is primarily Unstructured with viscous mesh near the airfoil and flap surfaces. This is crucial for accurately capturing the aerodynamic behavior, particularly the boundary layer effects and flow phenomena.

## Slide 12: CFD solver – SU2
Steady-state Reynolds-Averaged Navier-Stoken (RANS) equations.
      k −ω SST (Shear Stress Transport) – Two equation turbulence model.
          Better handling of adverse pressure gradients and flow separation.
          Enhanced near-wall resolution.
k: Turbulent kinetic energy (m2/s2)
ω: Specific Rate of Dissipation (1/s)
Notes: This research uses Steady state RANS equations coupled with KW SST turbulence model
PyAeroSweep is limited to steady state simulations, but the choice of KW SST turb model was made
due to it being a two-equation model
Handles adverse pressure gradient better
Favorable capturing of near wall effects

## Slide 13: Contents
  Tasks
  Objective
  Introduction
  Methodology
  Trade studies
  Results
  Summary
  Future work

## Slide 14: Optimization strategy
Fig 9: Fowler flap design optimization strategy.
OAT One-At-A-Time Optimization
Notes: As manual optimization was employed in this research, One at a time optimization means – varying one parameter and keeping the rest constant.
Find an optimum, change he values to optimum and then vary the rest.
As this research is only for flap design optimization, airfoil parameters were kept constant.
This was done until all the parameters were optimized and an optimized design with improved lift performance was obtained.

## Slide 15: Mesh sensitivity study
Fig 10: Impact of mesh refinement on maximum lift coefficient (CLmax ).
Table 2: Results of the mesh sensitivity study.
Fig 11: Effect of mesh refinement on grid resolution.
+0.27%
+0.71%
Notes: Mesh sensitivity study was performed to determine if the baseline mesh was sufficient to perform optimization studies.
30+ finer and 30- coarser mesh were compared
Coarser mesh to baseline - 0.71% improvement in Cl max – which is significant
Baseline to Fine – 0.27% - still significant, but comes at an increased simulation time
I used a normal workstation with basic PC configurations. Since I had to balance the practicality, accuracy and available computational resource, the baseline mesh offered a balance between these criteria's.

## Slide 16: Parameter sensitivity study
Table 3: Simulation freestream conditions and reference length (airfoil chord).
Table 4: Range of geometric parameters for the to-be optimized flap design.
Notes: Ranges – Chosen based on
Previous research data
Geometric feasibility through visual inspection
Tested for 15° first – Less Sensitivity
Moved on to 30° deflection
x_gap, y_gap showed more sensitivity

## Slide 17: Effect of variation of x_gap & y_gap on CD and CL varied across α:
Figure 12: Effect of variation of x_gap on CL vs α, with y_gap fixed at 4.0%
of the airfoil chord.
Figure 13: Effect of variation of y_gap on CL vs α, with x_gap fixed at 4.3% of the airfoil chord.
Baseline:
x_gap 3.0 % y_gap 1.5 %
Notes: x_gap varied – y_gap fixed
2.3% behaves similar to baseline at low AoA
y_gap varied – x_gap fixed
6% achieves higher Clmax as AoA increases

## Slide 18: Updated x_gap & y_gap
30° flap deflection
4° Angle of attack
2.43 % increase in CLmax
Fig 18: Baseline configuration
(x_gap at 3.0% & y_gap at 1.5% of the airfoil chord).
Fig 19: Updated configuration
(x_gap at 2.3% & y_gap at 6.0% of the airfoil chord).
Figure 17: Comparison of baseline and updated configuration
(x_gap at 2.3% and y_gap 6.0%).
Notes: Attempt was made to combine the effects
Performs better over the entire range of AoA

## Slide 19: Contents
  Tasks
  Objective
  Introduction
  Methodology
  Trade studies
  Results
  Summary
  Future work
Notes: The effect of x and y gaps on Cl max was significant
But, other parameters also helped in the overall optimization
Though, their individual contribution was comparatively less, their combined effect played a major role in maximizing the lift

## Slide 20: Results
Table 5: Baseline and optimized flap design parameters (in ratios).
Fig 20: Comparison of baseline and optimized airfoil and flap geometric profiles (all parameters optimized).
Notes: The table to the left showcases the optimized parameter values vs the baseline
The image to the right shows a comparison of he baseline, clean and the optimize design
The image in the bottom left of the Fowler flap shows noticeable changes to the leading edge and the conical parameters near the LE and on the suction side.

## Slide 21: Aerodynamic performance at 30-degree flap deflection
30° flap deflection
4° Angle of attack
4.56 % increase in
CLmax
Fig 22: Eddy viscosity: Baseline configuration.
Fig 23: Eddy viscosity: Optimized configuration
(all parameters optimized).
Figure 21: Comparison of baseline and optimized configuration (CL vs α).
Notes: Channel flow is cleaner
LE has less disturbed flow
Does not disturb the recirculation inside the flap cutout
Cleaner flow on the suction side

## Slide 22: Aerodynamic performance at 30-degree flap deflection
30° flap deflection
13° Angle of attack
4.56 % increase in
CLmax
Fig 25: Eddy viscosity: Baseline configuration.
Fig 26: Eddy viscosity Optimized configuration
(all parameters optimized).
Figure 21: Comparison of baseline and optimized configuration (CL vs α).
Notes: Even at higher AoA, the optimized flap continues to exhibit favorable flow around the flap.

## Slide 23: Contents
  Tasks
  Objective
  Introduction
  Methodology
  Trade studies
  Results
  Summary
  Future work
Notes: The analysis was also conducted for the 15-degree flap deflection with the optimized parameters and the following results were obtained.

## Slide 24: Summary
1000+ CFD runs, manually optimized and post-processed.
10 parameters varied.
Tested for:
    15° flap deflection.
    30° flap deflection.
Table 6: Summary of maximum lift coefficient (CLmax) improvements.

## Slide 25: Contents
  Tasks
  Objective
  Introduction
  Methodology
  Trade studies
  Results
  Summary
  Future work

## Slide 26: Future work
Unsteady Reynolds-Averaged Navier-Stokes (URANS).
Implementing:
    Surrogate-Based Optimization.
    Automatic Optimization Algorithms.

## Slide 27: References
[1] Jochen Wild. High-lift aerodynamics. CRC Press, 2022
[2] Henning Strüber. ‘The aerodynamic design of the A350 XWB-900 high lift system’. In: 29th international congress of the aeronautical sciences. International Council of the Aeronautical Sciences. 2014.
[3] Mauro Minervino, Pierluigi Iannelli and D. Quagliarella. ‘3D Flap Design using Navier- Stokes Equations and Evolutionary Optimization Techniques on an Industrial Platform’. In: Sept. 2011. doi: 10.13140/2.1.2211.0083.

## Slide 28: Thank you for listening.

## Slide 29: Eddy Viscosity
30° flap deflection
4° Angle of attack
Fig 14: Baseline configuration
(x_gap at 3.0% & y_gap at 1.5% of the airfoil chord).
Fig 15: Optimized configuration (x_gap at 2.3% & y_gap at 4.0% of the airfoil chord).
Fig 16: Optimized configuration (x_gap at 4.3% & y_gap at 6.0% of the airfoil chord).
Notes: Here
Baseline:
  Disturbed flow at LE,
  Disturbed Channel Flow,
  Disturbed Flow over the Flap Surface
x_gap at 2.3% & y_gap at 4.0%
  Excels in Maximizing CL max
x_gap at 4.3% & y_gap at 6.0%
  Showcases better flow characteristics
    On Flap’s Upper Surface & In the Flap Cutout

## Slide 30: Aerodynamic performance at 15-degree flap deflection

## Slide 31: Aerodynamic performance at 30-degree flap deflection